## Slide 1: Wildcat Valley Railway
Control Systems Nov 2020

## Slide 2
JMRI IMPLEMENTATION ON THE WVR
Control turnouts from JMRI panels, facia panels, throttles
Display block occupancy on JMRI control panels
Control the track signal system based on block occupancy using JMRI
Control layout lighting using JMRI and DMX512

## Slide 5
Overview of Block Detection and Turnout Control
This was my initial setup used to test the systems for viability. I am still using the RR-CirKits Tower Man board, but I have also installed a Tower Controller Mark II which interfaces directly to the Loconet bus. The Tower Man and TC Mark II are programmed using the JMRI Decoder Pro program.

## Slide 7
Semaphores respond to turnout commands from JMRI to set the aspect

## Slide 9
DMX 512 lighting control for LED strip lights
The Arduino with DMX shield receives turnout signals from the JMRI computer generated based on the JMRI fast clock. Additional turnout commands are used to change the mode.
Ethernet cables carry the dmx 512 signals to the receivers around the room which control the LED strips brightness.

## Slide 12
Servo Turnout Actuator
DCC Turnout Decoder

## Slide 20
VCC
GND
10
12
2
6
8
9
Arduino Connections

## Slide 22
https://github.com/DMASHINO/WVR-turnout-decoder
To Download a .zip folder

## Slide 24
NmraDcc Library must be installed
Google “Arduino NMRADCC”

## Slide 25
Upload the program to the Arduino using the FTDI breakout board and USB cable

## Slide 26
Two additional boards based on the simple DCC accessory decoder
Operates four single or double head semaphore signals with LED’s.
Control for a Rapido RailCrew uncoupler

## Slide 27
Thanks!
Contact info: dave@mashinos.com